## Slide 1: Test Challenges for 3D Integrated Circuits
ECE 7502 Class Discussion
Reza Rahimi
10th Feb 2015

## Slide 2
Requirements
Specification
Architecture
Logic / Circuits
Physical Design
Fabrication
Manufacturing Test
Packaging Test
PCB Test
System Test
PCB Architecture
PCB Circuits
PCB Physical Design
PCB Fabrication
Design and Test Development
Customer
Validate
Verify
Verify
Test
Test

## Slide 3: Test Challenges
  Lack of probe access for wafers
  Test access to modules in stacked wafers/dies
  Thermal concerns
  Design testability
  Test economics
  New defects arising from unique processing steps
    Wafer thinning
    Alignment
    Bonding
  Test-access and Test Scheduling

## Slide 4: How to build?
Monolithic
  Require many changes in current process facilities
Die Stacking
  Can minimize the impact of altering existing manufacturing technology and equipment
[1]
[1]
Not scalable. Limited to two layers

## Slide 5: How to increase yield?
Pretested Dies
Sort the wafers first and stack matched dies
  Speed
  Power
Obstacles
  Wafer probing
  Known good die
  New defect types
  Testing of the TSVs
  Thermal and Power-Delivery Considerations in Testing
  Test-access and Test Scheduling for Core-based SOCs
  Economics of Test and Its Relationship to Other Cost Factors:

## Slide 6: Wafer probing
Connection from the tester to the wafer
  Probing needles : Performance limit & cost contributor=>Lower frequency
  Probe card applies a force of 3-10 g per probe =>60-120 kg
    Contactless Probe
  Solution: Scan chain and DFT
[www.wikipedia.org]

## Slide 7: A contactless probe example[7]

## Slide 8: Wrapper cells
TSV
  Cylindrical copper nails providing electrical connection from active front-side of a silicon die through the silicon substrate to the back-side
  Prior to bonding, TSVs are not fully accessible because one of their ends is not connected to logic on other dies.
  The combinational part of die logic between the last level of scan cells and outbound TSVs cannot be observed, and that between inbound TSVs and first level of scan cells cannot be controlled.
  Solution: Wrapper cell
[3]

## Slide 9: Design for Testability
Tens of thousands TSVs
  Significant overhead.
  Higher latency.
  Performance degradation.
Problem:
[3]
[3]
[3]
[3]

## Slide 10: Cont’d
Considering scan flops for more than one TSV
Minimum number of wrappers
Timing constraint on flops at the ends of critical paths
Finding globally optimum solution(Minimum wrapper cell count).
NP-complete
  Heuristic algorithms.

## Slide 11: Converting to a graph problem
[3]

## Slide 12: TSV fault models
Left to Right:
  Fault Free
  Full Open (insufficient TSV filling).
  Micro void (insufficient TSV filling).
  Oxide pin-hole (silicon side wall imperfection).
[4]

## Slide 13: BIST for TSV Defects[4]
BIST Bock
Solution:
  Localizing FF clock with control signal.

## Slide 14: Cont’d
Can find d<0.99
[4]

## Slide 15: Parametric Fault Model[6]
Failure Analysis
  Understand the defect mechanism
Parameters
  R_driver: on-resistance of the driving gate of the TSV
  R_TSV: lumped series resistance of the TSV
  C_TSV: lumped capacitance of the TSV
  L_TSV: inductance of the TSV
  R_leak: resistance of a leakage path away from the TSV

## Slide 16: Parametric Fault Model[6]
Ring Oscillator
  Testing delay faults
  XOR gates: to make the test structure symmetric
  Opposite values to the enable inputs of the two XORs
Estimate the transition time by three steps
  First: both VOT inverters are in normal (oscillation period=T_ref)
  Second: TSV1’s VOT inverter is switched to Schmitt-Trigger mode (oscillation period=T_ST1)
  Third:TSV2’s VOT inverter is switched to Schmitt-Trigger mode (oscillation period=T_ST2)
  TSV1 delay has a linear relation with T_ST1-T_ref
  TSV2 delay has a linear relation with T_ST2-T_ref

## Slide 17: Parametric Fault Model[6]
Signature(T_ref,T_ST)
Define fault boundary based on process variation model using Monte-Carlo simulation

## Slide 18: Stacking[2]
Sequential or rearranged?
3D test flows for rearranged stacking[2]

## Slide 19: Power and Thermal Issues[5]
I/O pin limitation problem
New Technology
  Lower VDD
    Lower noise margin
  Higher current per pin
    Higher IR and L(di/dt) noise
3D IC
  Reduced footprint area
    Reduced interconnect wires
    Reduced the number of I/O pins too

## Slide 20: Power and Thermal Issues[5]
Stacked-VDD
  Balanced blocks
    Reduce current to 1/n of original value
    Noise and electro migration would be significantly alleviated
  Unbalanced blocks?

## Slide 21: Vdd Stacking Application in 3D-IC
Allocate a single Vdd value to each tier of the 3D IC.
  high-current blocks will be stacked up over each other
    Thermal issues
Algorithm
  Divide each tier to regions based on Regulators location
    Euclidean distance or any other metric.
    Assign a Vdd level to each module.
    Split down modules to sub-modules.
      Assign sub-modules in different regions but with same Vdd
    Use a low pass filter for I(t)

## Slide 22: Cont’t[5]

## Slide 23: Discussion questions
How does the contact-less probes work?
How can DFT help probing problem?
How can DFT help in finding Known Good Dies?
How BIST can help us in finding defects in TSVs?
How can we solve 3D-ICs thermal problem using VDD shifting?

## Slide 24: Papers
[1] Lee, H; Chakrabarty, K, "Test Challenges for 3D Integrated Circuits," Design & Test, IEEE , vol.PP, no.99, pp.1,1, 0 doi: 10.1109/MDT.2009.102
[2] Chang Hao; Liang Huaguo; Li Yang; Ouyang Yiming, "Optimized stacking order for 3D-stacked ICs considering the probability and cost of failed bonding," VLSI Design, Automation and Test (VLSI-DAT), 2014 International Symposium on , vol., no., pp.1,4, 28-30 April 2014
[3] Agrawal, M.; Chakrabarty, K., "A graph-theoretic approach for minimizing the number of wrapper cells for pre-bond testing of 3D-stacked ICs," Test Conference (ITC), 2013 IEEE International , vol., no., pp.1,10, 6-13 Sept. 2013
[4] Di Natale, G.; Flottes, M.-L.; Rouzeyre, B.; Zimouche, H., "Built-in self-test for manufacturing TSV defects before bonding," VLSI Test Symposium (VTS), 2014 IEEE 32nd , vol., no., pp.1,6, 13-17 April 2014
[5] Y. Zhan and S. Sapatnekar. Automated module assignment in stacked-vdd designs for high-efficiency power delivery. ACM Journal on Emerging Technologies in Computing Systems, 4(4), 2008
[6] Yu-Hsiang Lin; Shi-Yu Huang; Kun-Han Tsai; Wu-Tung Cheng; Sunter, S., "A unified method for parametric fault characterization of post-bond TSVs," Test Conference (ITC), 2012 IEEE International , vol., no., pp.1,10, 5-8 Nov. 2012

## Slide 25: Paper Map (e.g.)
[1] A survey on 3D IC Test
[2] stack reordering
Increase Yield
[3] Wrapper cell
A DFT method for 3D IC
[4] TSV Fault
A BIST method for 3D IC
[5] stack vdd
Assigning blocks to different vdd
[4] TSv Fault
A Parametric BIST method for 3D IC

## Slide 26: Glossary
…